## Slide 1
Start Serial
eeprom_init()
Start Ethernet
SD Card Manager
Start I2C Wire Int.
Scan the I2C Bus
Define Toggle Sw.
Define Turnouts
Define Sensors
Define Indicators
Initialize Serial Monitor Interface at 9600 baud
Scan EEPROM for invalid values
Initialize Ethernet card driver
Tests for the presence of a SD card in the Ethernet board;
If present, starts console with Arduino IDE – must reset when done
Initialize Wire class interface for I2C bus
Scan the I2C and identify devices and print to Serial Monitor
Read EEPROM and define turnouts controlled by toggle switches
Read EEPROM and define turnout names and set initial states
Read EEPROM and define sensor outputs from turnouts
Read EEPROM and define indicators driven by turnouts and sensors
Setup()
Define Keyboards
Read EEPROM and define keyboard for storage track and second comm line
Define Sensors
Read EEPROM and define sensor boards for block detectors
Define Signal Inputs
Read EEPROM and define local and remote inputs for signal logic
Define Signals
Read EEPROM and define signals on the layout